## Slide 1: Progress on Helical Undulator for Polarised Positron Production
Duncan Scott
ASTeC
Daresbury Laboratory
Presented by
Gudrid Moortgat-Pick

## Slide 2: Contents
Introduction
Helical Undulator Designs
  Super-Conducting
  Pure Permanent Magnet
Further Work

## Slide 3: Introduction
Looked at different helical undulator designs.
  Super-Conductin Wires
  Permanent Magnet Helical
  Planar Permanent Magnet Helical
Carrying out Engineering Feasibilty on two designs

## Slide 4: Super - Conducting Design
Magnet Design for 12 & 14mm periods:
  Vacuum Vessel Diameter 4mm
Calculated the magnetic field at the SC wires
For 12mm period this 83% of Critical Field
For 14mm period this 50% of Critical Field
  (cf at Critical Field wires become normal conducting)
Helix
Diameter
Undulator Period, u
Current, -i
Current, i
Notes: Electron Beam Passes through undulator and radiation is emitted
Electrons are accelerated by sinusoidal field and emit synchrotron radiation
NB There is constrictive interference which gives a peak radiation flux at a particular energy
Radiation hits target (electrons go to IP)
In target electron positron pairs are produced
Positrons are extracted

## Slide 5: Permanent Magnet Undulator Design
“Halbach” undulator (Klaus Halbach NIM Vol. 187, No1)
Rotate many rings to create Helical Field
PPM blocks create Dipole Field
Notes: 2nd Method: Create a rotating dipole field
Dipole field created by a ring of permanent magnet blocks with a rotating magnetisation vector
On axis helical field created by rotating the dipole rings 360 degrees along 1 period

## Slide 6: Permanent Magnet Undulator Design
Looking at 14mm period solution
Vacuum system difficult
Maximum vacuum for stainless steel pipe ~ 10-7 mbar
Therefore NEG coating will be needed
However NEG coating a 4mm diameter tube has never been done
Notes: As the  ray energy increases the rate of pair production increases
At high energies (>20MeV) cross section is constant
At very high energies (>30MeV) e+ have too much KE and are lost
 Require 20MeV Photons
Line on the graph shows the optimum on axis field / undulator period that maximises 20 MeV photon production

## Slide 7: Next - Steps
Super-Conducting
  Look at other periods & diameters
  Solutions for making the former
  Iron yoke and non iron vacuum vessel
Halbach
  Creating the required vacuum
  Engineering of magnet holders and alignment of rings
Build a prototype of preferred option (or one of each…?)
Notes: Halbach & SC are “better” in theory but more demanding technically.
SC Problems
  Quenching
  Services
  Wire and Field quality
Halbach problems
  Lots of little blocks - how can you hold them in place
  Radiation damage over time
Planar devices LESS FIELD!